Induced EMF

- A coil of 100 turns and area 2.0 m2 is placed at right angles to a magnetic field of flux density 0.1 T. What emf (voltage) will be induced if it is rotated through 90o in a time of 5.0s?

E 	= 	Δ N A B

Δ t

= 	100 x 2.0 x 0.1

5.0

E	=	4.0 V

- A horizontal wire of length 1.0 m is dropped vertically at a constant speed of 5.0 m.s-1 through a uniform horizontal magnetic field of strength 4.0 T. Calculate the emf induced.

E 	= 	Δ N A B

Δ t

=	1 x (1.0 x 5.0) x 4.0

1.0

(The wire moves 5.0 m in 1.0 s)

E	=	20 V